See Maps 1, 2, and 3.

The trail consists of six linear segments separated by three and boardwalks.  The following table specifies the locations of the endpoints of each segment.

| WAYPOINT | SEGMENT ENDPOINTS | GPS COORDINATES | DESIGN DRAWING | CUMULATIVE DISTANCE (FEET) |
| --- | --- | --- | --- | --- |
|  |  | LATITUDE | LONGITUDE |  |  |
| 001 | Pedestrian gate, northeast corner of parking lot. START SEGMENT 1 | 29.076350 | -95.427967 | None | 0 |
| 003 | END SEGMENT 1 Crossroads Junction START SEGMENT 2 | 29.076083 | -95.429067 | DWT-1 | 390 |
| 004 | END SEGMENT 2 South Bayou Junction START SEGMENT 3 | 29.076267 | -95.429567 | DWT-2 | 579 |
| 015 | END SEGMENT 3 Start Burl Oak Boardwalk | Staked | Staked | DWT-3 |  |
| 017 | End Burl Oak Boardwalk START SEGMENT 4 | Staked | Staked | DWT-3 |  |
| 022 | END SEGMENT 4 North Bayou Junction START SEGMENT 5 | 29.080667 | -95.430383 | DWT-4 | 2262 |
| 030 | END SEGMENT 5 Start North Boardwalk | 29.080800 | -95.430400 | DWT-5 | 2319 |
| 031 | End North Boardwalk START SEGMENT 6 | 29.080950 | -95.430250 | DWT-5 | 2394 |
| 003 | END SEGMENT 6 Crossroads Junction | 29.076350 | -95.427967 | DWT-1 | 4557 |

| WAYPOINT DEFINITIONS |
| --- |
| WAYPOINT | SEGMENT ENDPOINTS | DESIGN DRAWINGS | COMMENTS | CUMULATIVE DISTANCE (FEET) |
| 001 | Pedestrian gate, northeast corner of parking lot. | None | None | 0 |
| 003 | Crossroads Junction | DWT-1 | Identifies the entire junction | 390 |
| 004 | South Bayou Junction | DWT-2 | Identifies the entire junction | 579 |
| 015 | Burl Oak Boardwalk south end | DWT-3 | Boardwalk will be constructed by others prior to trail construction | 597 |
| 017 | Burl Oak Boardwalk north end | DWT-3 |  | 618 |
| 022 | North Bayou Junction | DWT-4 | Identifies the entire junction | 2262 |
| 030 | North Boardwalk east end | DWT-5 | Boardwalk will be constructed by others prior to trail construction | 2319 |
| 031 | North Boardwalk west end | DWT-5 |  | 2394 |

| SEGMENT WAYPOINTS | SEGMENT | GPS COORDINATES | DESIGN DRAWING | CUMULATIVE DISTANCE (FEET) |
| --- | --- | --- | --- | --- |
|  |  | LATITUDE | LONGITUDE |  |  |
| 001-003 | Pedestrian gate, northeast corner of parking lot. | 29.076350 | -95.427967 | None | 0 |
| 003 | Crossroads Junction | 29.076083 | -95.429067 | DWT-1 | 390 |
| 004 | South Bayou Junction | 29.076267 | -95.429567 | DWT-2 | 579 |
| 004-015 | Burl Oak Boardwalk | Staked | Staked | DWT-3 |  |
| 015-017 | Burl Oak Boardwalk | Staked | Staked | DWT-3 |  |
| 022 | North Bayou Junction | 29.080667 | -95.430383 | DWT-4 | 2262 |
| 030-031 | North Boardwalk | 29.080800 | -95.430400 | DWT-5 | 2319 |

Page xx of xx

ADA-Compliant Concrete Trail

The estimated total length of the concrete trail is 4425 feet.  This sum was derived as follows:

| Grand total length of trail including boardwalks | 4457 feet |
| --- | --- |
| Less length of Burl Oak Boardwalk | -57 |
| Less length of North Boardwalk | -75 |
| Total length of concrete trail | 4425 feet |

One or more PVC culverts as defined herein.

.

One or more runoff structures as defined herein.

A boardwalk as defined herein.

Friends of Brazoria Wildlife Refuges - Dow Woods Unit Restroom Specifications - 02/18/2010

Pa g e 4 o f 1 7

Section 2. Description of the Structure

The Structure shall include two side-by-side ADA-compliant private restrooms and a storage

room, oriented as shown in the Design Drawings.

Unless otherwise specified herein, each restroom shall comply with all applicable

requirements of the Americans with Disabilities Act as amended. Each restroom shall be

equipped as follows:

•	Waterless toilet with seat.

•	Impervious underground vault with a minimum capacity of 750 gallons.

•	Vault cleanout port.

•	Odor-free ventilation system.

•	Door as shown the Design Drawings.

•	Window as shown Design Drawings.

•	Ventilation screen as shown in Design Drawings.

•	Stainless steel grab bars

•	Framing as required to support grab bars.

•	Stainless steel toilet paper dispenser equipped with padlock hasp.

•	Stainless steel door hinges, latch, and lock.

Detail specifications:

•	Toilet risers, seats, and lids shall be constructed from polyolefin materials.

Associated hardware shall be stainless steel.

•	Single doors shall be 36" wide x 84" high. The double door at the rear of the building

shall be